## Slide 1: ESG Report – Phase 1 Ecological, Climate and Social Impact Assessment
Sun Mobility
February 2021

## Slide 2: Process Flow
1. Project Goals and Scope Definition
2. Life-Cycle Inventory Data Collection
3. Life Cycle Inventory Compilation
4.
Life-Cycle Inventory Analysis & Interpretation

## Slide 3: Assumptions
Assumptions
In-Use and not ‘rated’ Fuel Efficiency of Electric Vehicles (EVs) and Internal Combustion Engine Vehicles (ICEs) used; based on data supplied by Fleet Operators.
Renewable Energy contribution to electricity ‘fuel-mix’ accounted for in deriving Use-Phase GHG Emissions.
Material Acquisition and Pre-processing (including mining of rare earth metals, Lithium etc.) were not considered in this Phase and will be integrated in Phase 2 of the assessment process.
Emissions from mining, transporting, and distributions of fossil fuels (for ICEs and for non-renewable component of grid electricity were estimated and included in this Phase.
Emissions from Battery Production, End of Life processes for Vehicle Body (i.e. recycling, disposal etc. of metal, polymers, glass etc.), and Battery-Recycling were not considered in this Phase and will be integrated in Phase 2 of the assessment process.
Emissions from Distribution and Storage stage were considered to be negligible compared to other LCA stages and hence not included.

## Slide 4: Goal & Scope Definition
Goal
Establishing baseline life cycle carbon and air pollutant footprints for conventional (ICE), Lead-Acid EVs.
Conducting a comparative analysis, based on primary as well as secondary research, with the life cycle footprint of Sun Mobility’s Swappable Lithium-Ion Battery solutions (Battery-as-a-Service, Baas) for Electric Vehicle.
Provide high-caliber technical support for establishing a science-based voluntary self-disclosure centric financial and communications relationship with its customers and potential/current investors, through the results and insights derived from the comparative Life-Cycle-Analysis study of Sun Mobility's EV-mobility enabling products relative to Business-as-Usual mobility solutions prevalent in India in 2020.

## Slide 5: Goal & Scope Definition
Scope
Conduct comparative life cycle footprint analysis between EV and ICE Vehicles according to the life-cycle boundary defined below and analyze them through per vehicle-km travel scenario models.

## Slide 6: Goal & Scope Definition
Scope
PART 1: Primary Fuel Efficiency & Vehicle Research and Data Collection: Conducting primary and secondary research through literature reviews, interviews with stakeholders, web research catalogues to collate information on vehicle make, model, design and efficiency along with manufacturing and other details.
PART 2: Formulating Vehicle based Emission Factors: Thorough and comprehensive formulizing of vehicle-based emissions factors
PART 3: Conducting Life Cycle Assessments: Designing Spreadsheet models to calculate GHG and Non-Particulate Air Pollution mitigation assessments of Business-As-Usual and Intervention scenarios in accordance with the WRI GHG Protocol’s Product Life Cycle Accounting and Reporting Standard and the Scope 3 Emissions Accounting and Reporting Standard.

## Slide 7: Goal & Scope Definition
Scope
PART 4: Estimating Particulate Carbon (Black Carbon) Emissions and local air quality impacts in congruence with the Black Carbon Methodology for the Logistics Sector (2017) developed by the Global Green Freight Project’s Smart Freight Centre.
PART 5: Estimating the economic wellbeing benefits for materially relevant subsets of stakeholders/end-users of products in accordance with specific indicators and methodologies articulated in the Global Reporting Initiative’s ‘G4 Sustainability Reporting Guidelines’ relevant sections related to Economic Performance (G4 EC1 and EC4).

## Slide 8: Protocols & Standards
International Protocols followed:
1996 & 2006 IPCC Guidelines for National Greenhouse Gas Inventories, Vol. 2 – Energy for developing Scope 2 & Scope 3 Emission Factors for Indian Grid Electricity Mix.
EMEP/EEA Air Pollutant Emission Inventory Guidelines.
Greenhouse Gas Protocol’s Product Life Cycle Accounting and Reporting Standard (WRI, WBCSD).
Global Reporting Initiative’s ‘G4 Sustainability Reporting Guidelines.
Black Carbon Methodology for the Logistics Sector (2017), Global Green Freight Project.

## Slide 9: Table 1 – GHG Mitigation
Table 1: Greenhouse Gas Mitigation – upto 2025 (BAU Renewables % in Grid)
 |  | 2022 | 2023 | 2024 | 2025
Sr. No. | Vehicle Type | (tonnes CO2e) | (tonnes CO2e) | (tonnes CO2e) | (tonnes CO2e)
1 | Bus (Heavy Duty) - India | - | - | - | -
2 | Bus (Heavy Duty) - World | 2,872 | 29,519 | 105,649 | 248,656
3 | Scooter - India | 1,169 | 8,248 | 22,557 | 49,632
4 | Scooter - World | 24,380 | 98,418 | 225,039 | 455,147
5 | Three Wheeler (Freight) - India | 5,234 | 19,607 | 80,242 | 160,516
6 | Three Wheeler (Freight) - World | - | - | - | -
7 | Three Wheeler (Passenger) - India | 2,595 | 23,694 | 102,720 | 158,658
8 | Three Wheeler (Passenger) - World | 17,853 | 58,292 | 121,937 | 225,773
9 | Truck (Light Duty) - India | - | 4,559 | 47,703 | 129,877
10 | Truck (Light Duty) - World | - | 37,774 | 114,055 | 230,072
Total |  | 54,104 | 280,112 | 819,902 | 1,658,329
Cumulative |  | 54,104 | 334,216 | 1,154,119 | 2,812,448

## Slide 10: Table 2 – GHG Mitigation
Table 2: Greenhouse Gas Mitigation – upto 2025 (50% Renewables in Grid)
 |  | 2022 | 2023 | 2024 | 2025
Sr. No. | Vehicle Type | (tonnes CO2e) | (tonnes CO2e) | (tonnes CO2e) | (tonnes CO2e)
1 | Bus (Heavy Duty) - India | - | - | - | -
2 | Bus (Heavy Duty) - World | 2,872 | 29,519 | 105,649 | 248,656
3 | Scooter - India | 1,239 | 9,208 | 26,327 | 60,235
4 | Scooter - World | 24,380 | 98,418 | 225,039 | 455,147
5 | Three Wheeler (Freight) - India | 5,735 | 23,270 | 101,689 | 215,121
6 | Three Wheeler (Freight) - World | - | - | - | -
7 | Three Wheeler (Passenger) - India | 3,483 | 41,502 | 189,596 | 446,643
8 | Three Wheeler (Passenger) - World | 17,853 | 58,292 | 121,937 | 225,773
9 | Truck (Light Duty) - India | - | 5,258 | 58,177 | 166,245
10 | Truck (Light Duty) - World | - | 37,774 | 114,055 | 230,072
Total |  | 55,563 | 303,240 | 942,470 | 2,047,891
Cumulative |  | 55,563 | 358,803 | 1,301,273 | 3,349,164

## Slide 11: Context 1 – GHG Mitigation
Context 1: Greenhouse Gas Mitigation – by 2025
50% Renewables ~ adds 0.54 Million Tonnes CO2e benefit
Sun Mobility’s GHG Mitigation with BAU Grid ~ 2.8 Million Tonnes CO2e
Sun Mobility’s GHG Mitigation with 50% Renewables ~ 3.4 Million Tonnes CO2e
Sun Mobility’s GHG mitigation ~ 12 to 13 Million trees planted

## Slide 12: Chart 1 – GHG Mitigation
Chart 1: % Contribution to Greenhouse Gas Mitigation – in 2025 (BAU Renewables)
Chart: 
| Bus (Heavy Duty) - India | Bus (Heavy Duty) - World | Scooter - India | Scooter - World | Three Wheeler (Freight) - India | Three Wheeler (Freight) - World | Three Wheeler (Passenger) - India | Three Wheeler (Passenger) - World | Truck (Light Duty) - India | Truck (Light Duty) - World
 | 0 | 248656.4163 | 49631.5245 | 455146.5444 | 160515.6349 | 0 | 158658.0201 | 225772.6012 | 129876.5949 | 230071.5059

## Slide 13: Chart 2 – GHG Mitigation
Chart 2: % Contribution to Greenhouse Gas Mitigation – in 2025 (50% Renewables)
Chart: 
| Bus (Heavy Duty) - India | Bus (Heavy Duty) - World | Scooter - India | Scooter - World | Three Wheeler (Freight) - India | Three Wheeler (Freight) - World | Three Wheeler (Passenger) - India | Three Wheeler (Passenger) - World | Truck (Light Duty) - India | Truck (Light Duty) - World
 | 0 | 248656.4163 | 60235.3623 | 455146.5444 | 215120.6121 | 0 | 446642.8956 | 225772.6012 | 166244.7291 | 230071.5059

## Slide 14: Table 3 – NOx Mitigation
Table 3: NOx Mitigation – upto 2025 (BAU Renewables % in Grid)
 |  | 2022 | 2023 | 2024 | 2025
Sr. No. | Vehicle Type | (tonnes NOx) | (tonnes NOx) | (tonnes NOx) | (tonnes NOx)
1 | Bus (Heavy Duty) - India | - | - | - | -
2 | Bus (Heavy Duty) - World | 0 | 5 | 26 | 77
3 | Scooter - India | 2 | 13 | 36 | 79
4 | Scooter - World | 42 | 168 | 386 | 784
5 | Three Wheeler (Freight) - India | 6 | 23 | 93 | 186
6 | Three Wheeler (Freight) - World | - | - | - | -
7 | Three Wheeler (Passenger) - India | -1 | -10 | -14 | -119
8 | Three Wheeler (Passenger) - World | 17 | 57 | 121 | 226
9 | Truck (Light Duty) - India | - | 6 | 60 | 164
10 | Truck (Light Duty) - World | - | 57 | 172 | 348
Total |  | 66 | 318 | 878 | 1,745
Cumulative |  | 66 | 384 | 1,263 | 3,008

## Slide 15: Table 4 – NOx Mitigation
Table 4: NOx Mitigation – upto 2025 (50% Renewables in Grid)
 |  | 2022 | 2023 | 2024 | 2025
Sr. No. | Vehicle Type | (tonnes NOx) | (tonnes NOx) | (tonnes NOx) | (tonnes NOx)
1 | Bus (Heavy Duty) - India | - | - | - | -
2 | Bus (Heavy Duty) - World | 0 | 5 | 26 | 77
3 | Scooter - India | 2 | 15 | 45 | 104
4 | Scooter - World | 42 | 168 | 386 | 784
5 | Three Wheeler (Freight) - India | 7 | 31 | 143 | 316
6 | Three Wheeler (Freight) - World | - | - | - | -
7 | Three Wheeler (Passenger) - India | 1 | 32 | 191 | 566
8 | Three Wheeler (Passenger) - World | 17 | 57 | 121 | 226
9 | Truck (Light Duty) - India | - | 7 | 85 | 251
10 | Truck (Light Duty) - World | - | 57 | 172 | 348
Total |  | 69 | 373 | 1,169 | 2,672
Cumulative |  | 69 | 442 | 1,611 | 4,283

## Slide 16: Context 2 – NOx Mitigation
Context 2: NOx Mitigation – by 2025
50% Renewables ~ adds 1,275 Tonnes NOx benefit
Sun Mobility’s GHG Mitigation with BAU Grid ~
3,008 Tonnes NOx
Sun Mobility’s GHG Mitigation with 50% Renewables ~
4,283 Tonnes NOx

## Slide 17: Chart 3 – NOx Mitigation
Chart 3: % Contribution to NOx Mitigation – in 2025 (BAU Renewables)
Chart: 
| Bus (Heavy Duty) - India | Bus (Heavy Duty) - World | Scooter - India | Scooter - World | Three Wheeler (Freight) - India | Three Wheeler (Freight) - World | Three Wheeler (Passenger) - India | Three Wheeler (Passenger) - World | Truck (Light Duty) - India | Truck (Light Duty) - World
 | 0 | 77.1648 | 78.9761 | 783.5518 | 185.981 | 0 | -119.2722 | 226.3957 | 164.0143 | 348.2016

## Slide 18: Chart 4 – NOx Mitigation
Chart 4: % Contribution to NOx Mitigation – in 2025 (50% Renewables)
Chart: 
| Bus (Heavy Duty) - India | Bus (Heavy Duty) - World | Scooter - India | Scooter - World | Three Wheeler (Freight) - India | Three Wheeler (Freight) - World | Three Wheeler (Passenger) - India | Three Wheeler (Passenger) - World | Truck (Light Duty) - India | Truck (Light Duty) - World
 | 0 | 77.1648 | 104.2008 | 783.5518 | 315.877 | 0 | 565.795 | 226.3957 | 250.5279 | 348.2016

## Slide 19: Table 5 – Black Carbon Mitigation
Table 5: Black Carbon Mitigation – upto 2025 (BAU Renewables % in Grid)
 |  | 2022 | 2023 | 2024 | 2025
Sr. No. | Vehicle Type | (tonnes BC) | (tonnes BC) | (tonnes BC) | (tonnes BC)
1 | Bus (Heavy Duty) - India | - | - | - | -
2 | Bus (Heavy Duty) - World | 0.06 | 0.58 | 2.03 | 4.68
3 | Scooter - India | 0.00 | 0.00 | 0.00 | 0.01
4 | Scooter - World | 0.03 | 0.12 | 0.27 | 0.57
5 | Three Wheeler (Freight) - India | 0.14 | 0.51 | 2.06 | 4.08
6 | Three Wheeler (Freight) - World | - | - | - | -
7 | Three Wheeler (Passenger) - India | 0.02 | 0.23 | 0.94 | 1.58
8 | Three Wheeler (Passenger) - World | 0.00 | 0.01 | 0.02 | 0.05
9 | Truck (Light Duty) - India | - | 0.11 | 1.14 | 3.08
10 | Truck (Light Duty) - World | - | 0.71 | 2.13 | 4.27
Total |  | 0.25 | 2.26 | 8.59 | 18.32
Cumulative |  | 0.25 | 2.51 | 11.10 | 29.42

## Slide 20: Table 6 – Black Carbon Mitigation
Table 6: Black Carbon Mitigation – upto 2025 (50% Renewables in Grid)
 |  | 2022 | 2023 | 2024 | 2025
Sr. No. | Vehicle Type | (tonnes BC) | (tonnes BC) | (tonnes BC) | (tonnes BC)
1 | Bus (Heavy Duty) - India | - | - | - | -
2 | Bus (Heavy Duty) - World | 0.06 | 0.58 | 2.03 | 4.68
3 | Scooter - India | 0.00 | 0.01 | 0.02 | 0.07
4 | Scooter - World | 0.03 | 0.12 | 0.27 | 0.57
5 | Three Wheeler (Freight) - India | 0.14 | 0.53 | 2.18 | 4.39
6 | Three Wheeler (Freight) - World | - | - | - | -
7 | Three Wheeler (Passenger) - India | 0.03 | 0.33 | 1.42 | 3.17
8 | Three Wheeler (Passenger) - World | 0.00 | 0.01 | 0.02 | 0.05
9 | Truck (Light Duty) - India | - | 0.11 | 1.20 | 3.28
10 | Truck (Light Duty) - World | - | 0.71 | 2.13 | 4.27
Total |  | 0.26 | 2.38 | 9.27 | 20.48
Cumulative |  | 0.26 | 2.64 | 11.91 | 32.39

## Slide 21: Context 2 – NOx Mitigation
Context 2: NOx Mitigation – by 2025
50% Renewables ~ adds 3 Tonnes Black Carbon benefit
Sun Mobility’s GHG Mitigation with BAU Grid ~
29.4 Tonnes Black Carbon
Sun Mobility’s GHG Mitigation with 50% Renewables ~
32.4 Black Carbon

## Slide 22: Chart 5 – Black Carbon Mitigation
Chart 5: % Contribution to BC Mitigation – in 2025 (BAU Renewables)
Chart: 
| Bus (Heavy Duty) - India | Bus (Heavy Duty) - World | Scooter - India | Scooter - World | Three Wheeler (Freight) - India | Three Wheeler (Freight) - World | Three Wheeler (Passenger) - India | Three Wheeler (Passenger) - World | Truck (Light Duty) - India | Truck (Light Duty) - World
 | 0 | 4.6788 | 0.0071148 | 0.57059 | 4.0829 | 0 | 1.5769 | 0.049263 | 3.0829 | 4.2688

## Slide 23: Chart 6 – Black Carbon Mitigation
Chart 6: % Contribution to BC Mitigation – in 2025 (BAU Renewables)
Chart: 
| Bus (Heavy Duty) - India | Bus (Heavy Duty) - World | Scooter - India | Scooter - World | Three Wheeler (Freight) - India | Three Wheeler (Freight) - World | Three Wheeler (Passenger) - India | Three Wheeler (Passenger) - World | Truck (Light Duty) - India | Truck (Light Duty) - World
 | 0 | 4.6788 | 0.065868 | 0.57059 | 4.3855 | 0 | 3.1726 | 0.049263 | 3.2844 | 4.2688

## Slide 24: Context 4 – Economic Impact – EC1 (GRI)
Vehicle | Region | 2022 | 2023 | 2024 | 2025
E-Rick | India | 12 | 126 | 408 | 1,112
E-Auto | India | 6 | 57 | 213 | 471
Total | India | 18 | 183 | 621 | 1,584
E-Rick | World | 2 | 42 | 217 | 532
E-Auto | World | 3 | 51 | 265 | 650
Total | World | 5 | 93 | 482 | 1,183
Impact created (in million USD) – through E-Rickshaw/Auto Solution