## Slide 1: Consumption and footprint analysis of
India associates of
www.cbalance.in
www.bestfootforward.com

## Slide 2: Overview of the Hotel
Business hotel
5 Star
Hot & Humid climatic zone
No of rooms = 141
Average room tariff = Rs. 6400
Off-site laundry
Off-site waste water treatment (aerobic)
Year of analysis: 2011-2012
cBalance Solutions Hub

## Slide 3: Greenhouse Gas Inventory
*Not including corporate emissions
Chart: 
| Charcoal | Diesel | LPG | PNG | Refridgerants | Laundry | Electricity | Corporate emission | Dairy | Meat | Packaged Water | Solid Waste | Tanker Water | Muncipal Water
 | 58.79 | 26.615 | 38.085 | 147.01 | 1.5 | 163.84 | 3567.44 | 0 | 105.4 | 96.1 | 0.788 | 2.9 | 5.7 | 10.292
cBalance Solutions Hub

## Slide 4: Inventory by Scope & Benchmarks
85%
6%
9%
cBalance Solutions Hub
Total Footprint of hotel 4224.47 tCO2e
Benchmarks
0.12 tCO2e/overnight stay
0.34 tCO2e/square meter
29.9 tCO2e/room/year

## Slide 5: Peer based Comparison
In Top 2 percentile for overall energy efficiency
In Top 4 percentile for hotels in Hot & Humid area
In Top 9 percentile for all 5 star hotels
In Top 2 percentile for all business hotels
Chart: Tonnes CO2e
| Tonnes of CO2e /m2 | Tonnes of CO2e/overnight stay
5 Star | 0.40609 | 0.20432
4 Star | 0.50444 | 0.10179
3 Star | 0.34891 | 0.060556
2 Star | 0.22006 | 0.0275
cBalance Solutions Hub

## Slide 6: Results: Based on HCMI Methodology
Total CO2e for reporting period: 1263 tco2e
Total Guestrooms Carbon Footprint 919.34 tCO2e
Total Meetings Carbon Footprint 343.23 tCO2e
Footprint per occupied room on a daily basis 27.2 kgCO2e
Carbon footprint per area of meeting space on an hourly basis 94.0 kgCO2e
cBalance Solutions Hub

## Slide 7: Fuel Usage Pattern
Chart: Carbon Footprint (CO2e)
| Diesel | LPG | PNG
CO2e | 0.1256 | 0.17981 | 0.69459
Chart: Cost (INR)
| Diesel | LPG | PNG
Cost | 0.024751 | 0.017035 | 0.95821
cBalance Solutions Hub

## Slide 8: Water Inflow Pattern & Usage
Chart: Incoming Water
| Muncipal | Tanker | Rainwater | STP
Sales | 0.17703 | 0.55946 | 0.012384 | 0.25113
Quantity of water | 29069 KL
Associated emissions | 16.1 tCO2e
Chart: 
| Domestic water | Cooling Towers | Flushing | Gardening | Fire system
Water usage | 0.50001 | 0.23444 | 0.26445 | 0.013932 | 0.030077
cBalance Solutions Hub

## Slide 9: Waste
Chart: 
| Composting | Piggeries
Food Waste disposal | 0.095318 | 0.90468
Quantity of waste | 112.78 tonnes
Associated emissions | 2.9 tCO2e (composting)
cBalance Solutions Hub

## Slide 10: Laundry
Tent card helped save 2% of laundry
Laundry | 
Quantity of laundry | 639.96 tons
Associated emissions | 163.83 tCO2e
Emissions/ton | 260 kgCO2e/ton
Laundry | Savings
Electricity | 1460 kWh
Water | 480 KL
Furnace Oil | 700 l
GHG emissions | 4.4 tCO2e/year
cBalance Solutions Hub

## Slide 11: Solid Waste Management
Chart: Emissions Avoided
| Paper | Plastic | Glass | Metals
Sales | 0.42349 | 0.096085 | 0.037367 | 0.44306
Material | Quantity/year | Avoided Emissions (tCO2e)
Paper | 8491 kg | 23.8
Plastic | 3202 kg | 5.4
Glass | 9789 kg | 2.1
Metals | 2092 kg | 24.9
Cloth | 322 pieces | Reused as dusters
Total |  | 56.2
cBalance Solutions Hub

## Slide 12: Water Related Practices
Rainwater Capture Area=3130.55 sq m.
Campus Area = 1046sq m.
7% of captured rainwater is reused = 360 KL/year
93% of captured rainwater is recharged into the ground = 4782 KL/year
Activity Description | Key Performance Indicators
Rainwater Harvesting(Reuse) | 10% of campus area used
Rainwater Harvesting(Recharge) | 80% of campus area used
Managed Irrigation | 1082 l of water/square meter of garden/year
cBalance Solutions Hub

## Slide 13: Energy related Practices
Lighting Equipment Efficiency
Total Lighting Fixtures= 6157
CFL Fixtures= 1457
LED Fixtures= 4191
Energy Saving TFL Lighting= 509
Activity Description | Key Performance Indicators
CFL Lighting | 24%
LED Lighting | 68%
Energy Saving TFL Lighting | 8%
Lighting Equipment Efficiency
Total Lighting Wattage = 35159
CFL Wattage= 7599
LED Wattage= 17588
Energy Saving TFL Wattage= 5712
Activity Description | Key Performance Indicators
CFL Lighting | 22%
LED Lighting | 50%
Energy Saving TFL Lighting | 16%
cBalance Solutions Hub

## Slide 14: Energy related Practices
Energy efficient AC’s
Total Tonnage of split AC’s= 16 tonnes
10 Units
HVAC Efficiency
Total Tonnage of HVAC System = 1x125 TR = 375 TR
Activity Description | Key Performance Indicators
Thermo Storage | 100% of Tonnage
Activity Description | Key Performance Indicators
% tonnage from 3 star or above rate equipment | 50% of Tonnage
cBalance Solutions Hub

## Slide 15: Energy related Practices
F&B Energy Efficiency
Total Refrigeration Volume= 11500 liters Total Meals Served= 320586
Activity Description | Key Performance Indicators
Reduced Refrigeration | 0.036 Liters of Refrigeration/ Meal Served
Activity Description | Key Performance Indicators
Natural Lighting | 6 % BUA naturally Lit (daytime)
Solar Heat Gain Control | 100 % Double Glazed (BUA basis)
cBalance Solutions Hub
Architectural Energy Efficiency
Total Natural Light Area= 750.7 square meter
Activity Description | Key Performance Indicators
VFD Pumps | 24 % of Total Pumping Capacity
Equipment Energy Efficiency
Total Horse Power Of Pump= 215.5 Total Horse Power of VFD Pumps = 52.5

## Slide 16
Total Area covered by Building Management system= 3603 sq.m
Total Area Covered by Motion Controlled System= 5930 sq.m
Activity Description | Key Performance Indicators
BMS Controlled Area | 29% of BUA
Occupancy Controlled Area | 49% of low traffic BUA area
Power Factor Improvement System | 0.99 Average annual Power Factor
cBalance Solutions Hub
Equipment Energy Efficiency
Total Running length of hot and chilled Water pipes= 1280m
Activity Description | Key Performance Indicators
%(running meter) insulated hot/cold water piping | 100%
Energy related Practices

## Slide 17: Guest & Local Sustainable Activities
No guest sustainability activities
9 events conducted by staff during the year
Activity Description | Key Performance Indicators
Activities for economic development of local communities | 0 % of revenue
Activities for social development of local communities | <1 % of total man hours
Activities for environmental development of local communities | <1 % of total man hours
cBalance Solutions Hub

## Slide 18: Other significant Initiatives
Eco button :
The eco button provided in rooms which increases the temperature of the AC by 2 degrees was pressed 541 times in 6 months or approx. 1080 times in a year
Kitchen
  Induction stoves for buffet counters
  3 energy efficient self cooking centers from Rational
  De-frost freezers and clean fridges weekly to improve efficiency
  Peddle push for hand wash
Housekeeping
  4 bin method of segregation
  All garbage segregated at source
  Jute slipper, box etc provided in the rooms
F&B
  Neither Straws are being used nor paper napkin
  No coasters
  Glass bottles provided for water rather than bottled water & Don’t fill the full glass of water unless asked for
Management
  Email usage is mandated & Recycled paper is used for all stationary
cBalance Solutions Hub

## Slide 19: Additional points Observed
Excellent data collection in the Housekeeping and Engineering departments
All staff members very knowledgeable about sustainability initiatives within their department
cBalance Solutions Hub

## Slide 20: Potential room for Improvement
No sustainability initiatives involving guests
% of social development activities is very low
No norms for use of organic food
50% of split AC capacity is 3 star rated and the rest 2 star or lower
cBalance Solutions Hub